## Background

You are invited to assist in a study of the growth potential for microgeneration, including hydropower. The study is expected to help underpin future government and stakeholder policy setting (including any microgeneration targets) in this area through the provision of realistic estimates of uptake levels for the various microgeneration technologies as a function of various market conditions and policy interventions.

The present document contains a summary of technology cost projection and resource assumptions for hydropower that will form a key input into the model to predict uptake over time. The costs exclude the value of any grants.

Your feedback on the data below will help ensure any government support schemes – potentially including targets, grants, training schemes, marketing schemes and changes in regulations - are appropriate and adequately sized to achieve their desired goals. Please address your comments to Alex Stewart at Element Energy, (email to alex.stewart@element-energy.co.uk) or you can discuss by telephone on 01223 227 533. Comments should be received by 18th January 2008.

We would particularly welcome discussion on other factors, including awareness, understanding, reliability, ‘hassle’, and usability that form key elements of consumer decision making.

The work is funded and contracted through a steering board led by the Department of Business, Enterprise and Regulatory Reform (DBERR, former DTI), joined by a number of key stakeholder groups including the Ashden Trust, British Gas Service Ltd, Ceres Power plc, Energy Saving Trust, E.On UK plc, Micropower Council, National Energy Action, Renewable Energy Foundation, and the following Regional Development Agencies: North West Development Agency, East Midlands Development Agency, South West of England Development Agency, South East Development Agency and London Development Agency.

### Technology parameters

| Parameter | Value |
| --- | --- |
| Turbine efficiency | 85% |
| System efficiency (water to wire) | 70% |
| Load factor | 50% |
| Indicative size (domestic) | 5kW, 10kW |
| Indicative size (non-domestic) | 20kW, 50kW |
| Number of potential sites | 20,000 |

### Domestic System Cost Estimates

| Year | Marginal cost | Fixed cost | Maintenance Cost |
| --- | --- | --- | --- |
|  | £ / kWe | £ / installation |  |
|  | High head | Low head | High head | Low head | £ / yr |
| 2007 | £2,500 | £4,000 | £10,000 | - | £220 |
| 2020 | £2,300 | £3,700 | £10,000 | - | £220 |
| 2050 | £2,000 | £3,200 | £10,000 | - | £220 |

- Maintenance costs are based on a half day inspection/service once a year.

### Non-domestic System Cost Estimates

| Year | Marginal cost | Fixed cost | Maintenance Cost |
| --- | --- | --- | --- |
|  | £ / kWe | £ / installation |  |
|  | High head | Low head | High head | Low head | % of capex |
| 2007 | £1,500 | £2,000 | - | - | 1-2% |
| 2020 | £1,818 | £1,818 | - | - | 1-2% |
| 2050 | £1,666 | £1,666 | - | - | 1-2% |

# Footnotes

The scope of this study relates to system sizes that fall within the definition of microgeneration in the Microgeneration Strategy, i.e. up to 50kWe